Review of surface propagation studies in Moore's Bay, and other calculations
Jordan Hanson
CCAPP
February 24th, 2017

---
Outline
- Explanation of an experiment conducted in Moore's Bay, 2011-12
  - Motivation
  - Setup
  - Results
- Theoretical calculations (Fermat's principle)
- Reading: “Radio surf in polar ice: A new method of ultrahigh energy neutrino detection.” J. Ralston, Phys. Rev. D 71 011503 (2005)

---
Moore's Bay Surface Propagation Experiment

---
Moore's Bay Surface Propagation Experiment

---
Moore's Bay Surface Propagation Experiment
%DELTA = %DELTA t_{ "prop" } - %DELTA t_{ sys } = n %DELTA x/c - %DELTA t_{ sys } newline newline n = c(%DELTA + %DELTA t_{sys})/%DELTA x newline newline %sigma_{ n } = {c} over {%DELTA_{x}} sqrt { %sigma_{%DELTA}^2 + %sigma_{T}^2 + left(%sigma_x over x right)^2(%DELTA + %DELTA t_{sys})^2}
Component	Delay (ns)
RG-58	4.0
10 m LMR-600	38
20 m LMR-600	76
RG-8X	2134
PCD	10
Results: Δ = 360+/-10 ns, Δtsys = 1964 ns
n = 1.29+/-0.02
(No one source of error dominates).

---
Data Acquired

---
Theoretical Calculations (see report on Dropbox)
Fermat's Principle
Straight rays
Surface
y
-z
Deep Ice

---
Theoretical Calculations (see report on Dropbox)
Measured index profiles in Antarctica

---
Theoretical Calculations (see report on Dropbox)

---
Theoretical Calculations (see report on Dropbox)
Definitions:
1) Derivatives are with respect to z
2) u = dy/dz
3) z0 is the same from n(z)
Limiting Cases:
a) Deep ice: straight lines
b) Surface, ~horizontal: quadratic
c) Shallow: quadratic

---
Wait for it...If z_0 is the quadratic curvature, and that number is measured to be larger for Moore's Bay, paths should be bent MORE in Moore's Bay.
They are not, apparently. Or, at least some portion of the wave is not.
So although my analytic model of ray-tracing is fast, simple, and based on Fermat's principle, it's not entirely correct.

---
Conclusions
- Explanation of an experiment conducted in Moore's Bay, 2011-12
  - Motivation – Looking for surface propagation
  - Setup – 540 meter baseline
  - Results – Prompt and Delayed Components propagated along surface
- Theoretical calculations: Fermat's principle tells us that if there is a solution between two points, the fastest path between them for firn is roughly quadratic.
- Reading: “Radio surf in polar ice: A new method of ultrahigh energy neutrino detection.” J. Ralston, Phys. Rev. D 71 011503 (2005)